## Slide 1
There are several differences in terminology between AMD (formerly Xilinx) and Intel (formerly Altera) FPGA tools. Here are some of the key terms

## Slide 2
1. Device Families:
- AMD(Xilinx): Spartan, Virtex, Kintex, Artix, Zynq
- Intel (Altera): Cyclone, Stratix, Arria, Max
2. Design Tools:
- AMD(Xilinx): Vivado, ISE (older)
- Intel (Altera): Quartus Prime, Quartus II (older)
3. Programming Language:
- Both use VHDL and Verilog for design entry.
4. IP Cores:
- AMD(Xilinx): IP Integrator (IP), CORE Generator (older)
- Intel (Altera): Platform Designer (formerly Qsys), MegaCore Functions
5. Configuration Files:
- AMD(Xilinx): .bit (bitstream)
- Intel (Altera): .sof (SRAM Object File), .pof (Programmer Object File for Flash)

## Slide 3
6. Constraints Files:
- AMD(Xilinx): XDC (Xilinx Design Constraints)
- Intel (Altera): SDC (Synopsys Design Constraints)
7. Logic Cells/Elements:
- AMD(Xilinx): Logic Cells
- Intel (Altera): Logic Elements (LEs)
8. Block RAM:
- AMD(Xilinx): BRAM (Block RAM)
- Intel (Altera): M10K, M20K (depending on the device family)
9. DSP Blocks:
- AMD(Xilinx): DSP48
- Intel (Altera): DSP Blocks
10. Clock Management:
- AMD(Xilinx): MMCM (Mixed-Mode Clock Manager), PLL (Phase-Locked Loop)
- Intel (Altera): PLL (Phase-Locked Loop)

## Slide 4
11. Debugging Tools:
- AMD(Xilinx): Chipscope (older), Vivado Logic Analyzer
- Intel (Altera): SignalTap Logic Analyzer
12. Timing Analysis:
- AMD(Xilinx): Timing Constraints Wizard, Vivado Static Timing Analysis
- Intel (Altera): TimeQuest Timing Analyzer
13. Power Analysis:
- AMD(Xilinx): XPower Analyzer
- Intel (Altera): PowerPlay Power Analyzer

## Slide 5
Few more

## Slide 6
AMD(Xilinx):
Configurable Logic Block (CLB):
Contains multiple slices.
Each CLB typically consists of two slices.
Slice:
A slice is part of a CLB.
Contains several LUTs, flip-flops, carry logic, and multiplexers.
Intel (Altera):
Logic Array Block (LAB):
Contains several Adaptive Logic Modules (ALMs).
Each LAB typically consists of 10 ALMs.
Adaptive Logic Module (ALM):
An ALM is part of a LAB.
Contains two combinational logic elements (LEs).
Each LE can be configured as a 4-input LUT, two 3-input LUTs, and associated flip-flops, arithmetic logic, and carry chain.

## Slide 7
I/O Blocks:
Xilinx: I/O Blocks or I/O Banks
Intel (Altera): I/O Elements (IOE)
Clock Management Tiles:
Xilinx: Clock Management Tile (CMT), containing PLLs and MMCMs
Intel (Altera): PLLs for clock management
Embedded Multipliers:
Xilinx: DSP48 slices for DSP and arithmetic functions
Intel (Altera): Dedicated DSP Blocks for arithmetic functions
Memory Blocks:
Xilinx: Block RAM (BRAM)
Intel (Altera): MLAB (Memory Logic Array Blocks), M9K, M10K, M20K (depending on the device family)
Hard IP Cores:
Xilinx: Specific hard IP cores embedded in the FPGA fabric, like PCIe blocks, Multi-Gigabit Transceivers (MGT)
Intel (Altera): Specific hard IP cores such as PCIe, and high-speed transceivers

## Slide 8
Development Suites:
AMD(Xilinx): Vivado Design Suite, ISE Design Suite (older)
Intel (Altera): Quartus Prime, Quartus II (older)
Logic Design Units:
AMD(Xilinx): Logic Cell (LC)
Intel (Altera): Logic Element (LE)
Programming and Configuration:
AMD(Xilinx): JTAG, SelectMAP, Serial configuration modes
Intel (Altera): JTAG, AS (Active Serial), PS (Passive Serial) configuration modes
Hard Processor System:
AMD(Xilinx): Zynq-7000 and Zynq UltraScale+ MPSoC with ARM Cortex-A9 and ARM Cortex-A53 processors
Intel (Altera): SoC FPGAs with ARM Cortex-A9 processors