## Slide 1
Describes the hardware functionality of the Digital Systems in the textual form
It resembles programming language, but is specially developed for describing the functionality of the Digital hardware
The main difference with other high-level languages is
    HDL’s constructs ability to perform parallel execution
    Unlike sequential execution nature of other language constructs
Two HDLs are widely used
    Verilog HDL
    VHDL(Very High Speed Integrated Circuit HDL)
INTRODUCTION TO HDL- HARDWARE DESCRIPTION LANGUAGE

## Slide 2: LEXICAL CONVENTIONS
Verilog is a free-format language
  Like C language
White space (blank, tab, newline) can be used freely
Verilog is a case-sensitive language
Identifiers
  An identifier is used as an object reference. An identifier can contain a sequence of letters, digits, underscores (_) and dollar signs ($). The first character of an identifier can only be a letter or an underscore. Identifiers are case sensitive.
  User-provided names for Verilog objects in the descriptions
  Legal characters are “a-z”, “A-Z”, “0-9”, “_”, and “$”
    First character has to be a letter or an “_”
  Example: Count, _R2D2, FIVE$

## Slide 3: LEXICAL CONVENTIONS –Contd.
Keywords
  Predefined identifiers to define the language constructs
  All keywords are defined in lower case
  Cannot be used as idenfiers
  Example: initial, assign, module

## Slide 4: LEXICAL CONVENTIONS –CONT’D
Comments: two forms
/* First form:
can extend
over many lines */
// Second form: ends at the end of this line
Strings
– Enclosed in double quotes and must be specified in one line
  • “Sequence of characters”
Accept C-liked escape character
  • \n = newline
  • \t = tab
  • \\ = backslash
  • \” = quote mark (“)
  • %% = % sign

## Slide 5: LEXICAL CONVENTIONS –CONT’D
System tasks / function
  Execute the built-in tasks and functions
  Frequently used system tasks / functions
    $time: report the current simulation time
    $display: display the values of signals
    $monitor: continuously monitor the values of signals
    $stop: stop the simulation
    $finish: quit the simulation
Compiler directive
  Remain active through the rest of compilation until they are overridden or deactived
  Frequently used compiler directives
    `define<name><macro_text>:
    <name>will substitute<macro_text> at compile time
    `include<file_name> :
    include the contents of the file named as<file_name>

## Slide 6: INTEGER NUMBERS
Sized integers
  For unsigned integers only
  Representation form: [<size>] ‘ <base><value>
    where
      <size> is the size in bits (can be ignored)
      <base> can be b(binary), o(octal), d(decimal), or h(hexadecimal)
      <value> is any legal number in selected base and X(unknown), Z(high-impedence) (binary only)
      Example: `o721 (9-bit octal), 4’d2 (4-bit decimal)
        4’bz (4-bit z, z extended)
Unsized integers
  Signed decimal integers in two’s complement form
  Example: 32 (decimal 32), -15 (decimal -15)

## Slide 7: REAL NUMBERS
Decimal notation
11.2
1.572
0.1
Scientific notation
235.1e2 23510.0
3.6E2 360.0 (e is the same as E)
5E-4 0.0005
Must have at least one digit on either side of decimal
Stored and manipulated in double precision (usually 64-bits)

## Slide 8: VALUE SET
0: logic-0 / FALSE
1: logic-1 / TRUE
x: unknown / don’t care, can be 0, 1 or z
z: high-impedance

## Slide 9: DATA TYPES
Nets
  Connects between structural elements
  Values come from its drivers
    Continuous assignment
    Module or gate instantiation
  If no drivers are connected to net, default value is Z
Registers
  Represent abstract data storage elements
  Manipulated within procedural blocks
  The value in a register is saved until it is overridden
  Default value is X

## Slide 10: NET TYPES
wire, tri: standard net
wor, trior: wired-or net
wand, triand: wired-and net
trireg: capacitive
If all drivers at z, previous value is retained
tri1: pull up (if no driver, 1)
tri0: pull down (if no driver, 0)
supply0: ground
supply1: power
A net that is not declared defaults to a 1-bit wire
    wire reset;
    wor [7:0] DBUS;
    supply0 GND;

## Slide 11: REGISTER TYPES
reg: any size, unsigned
integer: 32-bit signed (2’s complement)
time: 64-bit unsigned
real, realtime: 64-bit real number
  Defaults to an initial value of 0
Examples:
  reg CNT;
  reg [31:0] SAT;
  integer A, B, C; // 32-bit
  real SWING;
  realtime CURR_TIME;
  time EVENT;

## Slide 12: PARAMETERS
Constant
Can be modified at compilation time
  Use defparam statement
Examples:
  parameter LINE_LENGTH = 132, ZLL_X_S = 16’bx;
  parameter BIT = 1, BYTE = 8, PI = 3.14;
  parameter SROBE_DELAY = (BYTE + BIT) / 2;
  parameter TQ_FILE = “/home/jimmy/TEST/add.tq”;
Common usage
  Specify delays and widths

## Slide 13: MEMORIES
Array of registers
No multiple dimensions
  reg [3:0] MY_MEM [0:63]; // 64 4-bit registers
Entire memory cannot be assigned a value in a single assignment
  reg [1:5] DIG; // 5-bit register
  DIG = 00000
  reg BOG [1:5]; // 5 1-bit register
  {BOG[1], BOG[2], …, BOG[5]} = 00000;
Can load memory by using a system task
  $readmem<base>(“<filename>”,<memory_name>,<start_addr>,<finish_addr>);
  where <base> can be b(binary) or h(hexadecimal)

## Slide 14: DIFFERENT LEVELS OF ABSTRACTIONS TO DESCRIBE THE FUNCTIONALITY OF THE HARDWARE
Switch-level modeling
Gate-level modeling
Dataflow-level modeling
Behavioural modeling
Structural modeling
Mixed level modeling

## Slide 15: SWITCH-LEVEL MODELING
SWITCH-LEVEL PRIMITIVES |  | 
MOS TRANSISTOR SWITCHES | MOS PULL GATES | MOS BIDIRECTIONAL SWITCHES
nmos | pullup | tran
pmos | pulldown | tranif0
cmos |  | tranif1
rnmos |  | rtran
rpmos |  | rtranif0
rcmos |  | rtranif1

## Slide 16: PRIMITIVES FOR MOS TRANSISTORS
nmos, pmos
rnmos, rpmos (resistive version)
Terminal list: (drain, source, gate)
(i.e., (output,input, control))

## Slide 17: EXAMPLE: INVERTER
(a) CMOS circuit, (b) in = 0, (c) in = 1

## Slide 18: VERILOG MODEL FOR CMOS INVERTER
module cmos_inverter (inv_out, inv_in);
output inv_out;
input inv_in;
supply0 GND;
supply1 PWR;
pmos (inv_out, PWR, inv_in);
nmos (inv_out, GND, inv_in);
endmodule

## Slide 19: EXAMPLE: 3-INPUT NAND GATE

## Slide 20: GATE-LEVEL MODELING
Gate-level Primitives |  | 
Multi-input Gates | Multi-output Gates | Three-state Gates
and | buf | bufif0
nand | not | bufif1
or |  | notif0
nor |  | notif1
xor |  | 
xnor |  | 

## Slide 21: TO VERIFY TRUTH TABLE AND WAVEFORMS OF LOGIC GATES USING GATE LEVEL MODEL
module allgates(inverter_out, and_out, nand_out, or_out, nor_out, exor_out, exnor_out, vin1, vin2);
input vin1, vin2;
output inverter_out, and_out, nand_out, or_out,
nor_out, exor_out, exnor_out;
not inverter1(inverter_out,vin2);
and and1(and_out,vin1,vin2);
nand nand1(nand_out,vin1,vin2);
or or1(or_out,vin1,vin2);
nor nor1(nor_out,vin1,vin2);
xor xor1(exor_out,vin1,vin2);
xnor xnor1(exnor_out,vin1,vin2);
endmodule

## Slide 22: TESTBENCH LOGIC GATES:
`timescale 1 ns / 1 ps
module test;
reg vin1, vin2;
wire inverter_out_vin2, and_out, nand_out, or_out, nor_out, exor_out, exnor_out;
integer i;
allgates ag(inverter_out_vin2, and_out, nand_out, or_out, nor_out, exor_out, exnor_out, vin1, vin2);
initial
for(i=0;i<4;i=i+1)
begin
{vin1,vin2}=i;
#5 ;
end
endmodule

## Slide 23: TYPES OF PORT ASSOCIATION/MAPPING/BINDING IN VERILOG HDL
There are 2 types
  positional
  named

## Slide 24: 1. POSITIONAL
//Binary 1-bit Half Adder
module ha(a,b,sum,co); //actual module
input a,b;
output sum,co;
assign sum = a^b;
assign co = a&b;
endmodule

## Slide 25: 1. POSITIONAL –Cont’d
When you want to instantiate the above module in Testbench or any Higher level module(for example Binary Full Adder using Half Adder)
You will be doing the following
  module name
  module instantiation name
  port list, such as shown below
module ……;/*It may be testbench or any other higher level module*/
//x,y,sum_result and carry_out are ports in the current module
ha h1(x,y,sum_result,carry_out);//instantiated module
endmodule
If you observe carefully the port list order is same in instantiated module and in the actual module .

## Slide 26: 2. NAMED
module ……..; /*It may be testbench or any other higher level module*/
……..
………
// x, y, sum_result and carry_out are ports in the current module
ha h1(.co(carry_out), .b(y), .sum(sum_result), .a(x)); //instantiated module
……..
…….
endmodule

## Slide 27: 1-BIT BINARY HALF ADDER --GATE LEVEL MODELING
module ha(a,b,sum,co);
input a,b;
output sum,co;
xor (sum,a,b);
and (co,a,b);
endmodule

## Slide 28: TESTBENCH: 1-BIT BINARY HALF ADDER
`timescale 1ns/1ps
module ha_test;
reg a,b;
wire sum,co;
ha hadder(a,b,sum,co); /*INSTANTIATE THE MODULE NAME(ha) THAT NEEDS BE TESTED WITH INSTANTIATION NAME hadder*/
initial
begin
{a,b} = 2’b00;
#5 {a,b} = 2’b01;
#5 {a,b} = 2’b10;
#5 {a,b} = 2’b11;
#5 $finish;
end
initial
$monitor($time, “a=%b, b=%b, sum=%b, co=%b” , a, b, sum, co);
endmodule

## Slide 29: DATA FLOW MODELING -- OPERATORS

## Slide 30
WIRED-AND CONFIGURATION

## Slide 31
wired logic A form of digital logic in which some logic functions are implemented by directly connecting together the outputs of one or more logic gates. The success of this technique depends on the electronic characteristics of the gates involved. The technique is commonly used in bus communication systems with tri-state output or with open-collector devices.
open-collector device A particular implementation of an electronic logic device in which the output of the device is formed by the open-circuit collector termination of the output transistor (see diagram). The device's output is thus active-low and a pull-up resistor is required to establish the active-high state. These devices are used to drive loads with high supply voltages or to implement wired-logic buses.
pull-up resistor A resistor that is connected between the power-supply line and a logic line and ensures that the line is normally pulled up to the supply potential. Open-collector logic devices may be connected to the logic line and each device is then capable of pulling the line low, i.e. to ground.
tri-state output (three-state output) An electronic output stage consisting of a logic gate, commonly an inverter or buffer, that exhibits three possible logic states, namely logic 1, logic 0, and an inactive (high-impedance or open-circuit) state. The inactive state allows the device outputs to be combined with other similar outputs in a busing structure such that only one device is active on the bus at any one time.
WIRED-LOGIC