## Slide 1
Parameters are Verilog constructs that allow a module to be reused with a different specification
For example, a 4-bit adder can be parameterized to accept a value for the number of bits and new parameter values can be passed in during module instantiation
So, an N-bit adder can become a 4-bit, 8-bit or 16-bit adder
They are like arguments to a function that are passed in during a function call
Parameters are basically constants and hence it's illegal to modify their value at runtime
It is illegal to redeclare a name that is already used by a net, variable or another parameter
There are two major types of parameters, module and specify and both accepts a range specification
But, they are normally made as wide as the value to be stored requires them to be and hence a range specification is not necessary
PARAMETERS

## Slide 2
parameter MSB = 7; // MSB is a parameter with a constant value 7
parameter REAL = 4.5; // REAL holds a real number
parameter FIFO_DEPTH = 256, MAX_WIDTH = 32; // Declares two parameters
parameter [7:0] f_const = 2'b3; // 2 bit value is converted to 8 bits; 8'b3
PARAMETERS –Cont’d

## Slide 3
Module parameters can be used to override parameter definitions within a module and this makes the module have a different set of parameters at compile time
A parameter can be modified with the defparam statement or in the module instance statement
It is a common practice to use uppercase letters in names for the parameter to make them instantly noticeable
The module shown below uses parameters to specify the bus width, data width and the depth of FIFO within the design, and can be overriden with new values when the module is instantiated or by using defparam statements
MODULE PARAMETERS

## Slide 4
// Verilog 1995 style port declaration
module design_ip ( addr,
wdata,
write,
sel,
rdata);
parameter BUS_WIDTH = 32,
DATA_WIDTH = 64,
FIFO_DEPTH = 512;
input addr;
input wdata;
input write;
input sel;
output rdata;
wire [BUS_WIDTH-1:0] addr;
wire [DATA_WIDTH-1:0] wdata;
reg [DATA_WIDTH-1:0] rdata;
reg [7:0] fifo [FIFO_DEPTH];
// Design code goes here ...
endmodule
MODULE PARAMETERS –Cont’d

## Slide 5
In the new ANSI style of Verilog port declaration, you may declare parameters as show below.
module design_ip
#(parameter BUS_WIDTH=32,
parameter DATA_WIDTH=64) (
input [BUS_WIDTH-1:0] addr,
// Other port declarations
);
MODULE PARAMETERS –Cont’d

## Slide 6
Parameters can be overridden with new values during module instantiation.
The first part instantiates the module called design_ip by the name d0 where new parameters are passed in within #()
The second part uses a Verilog construct called defparam to set the new parameter values
The first method is the most commonly used way to pass new parameters in RTL designs
The second method is commonly used in testbench simulations to quickly update the design parameters without having to reinstantiate the module
OVERRIDING PARAMETERS

## Slide 7
module tb;
// Module instantiation override
design_ip #(BUS_WIDTH = 64, DATA_WIDTH = 128) d0 ( [port list]);
// Use of defparam to override
defparam d0.FIFO_DEPTH = 128;
endmodule
OVERRIDING PARAMETERS –Cont’d

## Slide 8
The module counter has two parameters N and DOWN declared to have a default value of 2 and 0 respectively
N controls the number of bits in the output effectively controlling the width of the counter. By default it is a 2-bit counter
Parameter DOWN controls whether the counter should increment or decrement. By default, the counter will decrement because the parameter is set to 0
EXAMPLE-1 : 2-bit up-counter

## Slide 9
module counter
#( parameter N = 2,
parameter DOWN = 0)
( input clk,
input rstn,
input en,
output reg [N-1:0] out);
always @ (posedge clk) begin
if (!rstn) begin
out <= 0;
end else begin
if (en)
if (DOWN)
out <= out - 1;
else
out <= out + 1;
else
out <= out;
end
end
endmodule
EXAMPLE-1 : 2-bit up-counter --Cont’d

## Slide 10
The module counter is instantiated with N as 2 even though it is not required because the default value is anyway 2
DOWN is not passed in during module instantiation and hence takes the default value of 0 making it an up-counter
module design_top ( input clk,
input rstn,
input en,
output [1:0] out);
counter #(.N(2)) u0 ( .clk(clk),
.rstn(rstn),
.en(en));
endmodule
EXAMPLE-1 : 2-bit up-counter --Cont’d

## Slide 11
See that default parameters are used to implement the counter where N equals two making it a 2-bit counter and DOWN equals zero making it an up-counter
The output from counter is left unconnected at the top level
EXAMPLE-1 : 2-bit up-counter --Cont’d

## Slide 12
In this case, the module counter is instantiated with N as 4 making it a 4-bit counter
DOWN is passed a value of 1 during module instantiation and hence an down-counter is implemented
EXAMPLE-2: 4-BIT DOWN-COUNTER
module design_top ( input clk,
input rstn,
input en,
output [3:0] out);
counter #(.N(4), .DOWN(1))
u1 ( .clk(clk),
.rstn(rstn),
.en(en));
endmodule

## Slide 13
PARAMETERS
In Verilog HDL, parameters are constants and do not belong to any other data type such as net or register data types
You are not allowed to modify parameter values at runtime, but you can modify a parameter value using the defparam statement
The defparam statement can modify parameters only at the time of compilation
Parameter values can also be modified using #delay specification with module instantiation
In Verilog there are two ways to override a module parameter value during a module instantiation
The first method is by using the defparam keyword and
the second method is called module instance parameter value assignment

## Slide 14
A parameter is defined by Verilog as a constant value declared within the module structure. The value can be used to define a set of attributes for the module which can characterize its behavior as well as its physical representation
Defined inside a module
Local scope
Maybe overridden at instantiation time
  If multiple parameters are defined, they must be overridden in the order they were defined. If an overriding value is not specified, the default parameter declaration values are used.
Maybe changed using the defparam statement
PARAMETERS –Cont’d

## Slide 15
module secret_number;
parameter my_secret = 0;
initial begin
$display("My secret number is %d", my_secret);
end
endmodule
module defparam_example();
defparam U0.my_secret = 11;
defparam U1.my_secret = 22;
secret_number U0();
secret_number U1();
endmodule
PARAMETER OVERRIDE USING DEFPARAM

## Slide 16
1 module ram_sp_sr_sw (
2 clk , // Clock Input
3 address , // Address Input
4 data , // Data bi-directional
5 cs , // Chip Select
6 we , // Write Enable/Read Enable
7 oe // Output Enable
8 );
10 parameter DATA_WIDTH = 8 ;
11 parameter ADDR_WIDTH = 8 ;
12 parameter RAM_DEPTH = 1 << ADDR_WIDTH;
13 // Actual code of RAM here
14
15 endmodule
PASSING MORE THAN ONE PARAMETER

## Slide 17
module secret_number;
parameter my_secret = 0;
initial begin
$display("My secret number in module is %d", my_secret);
end
endmodule
module param_overide_instance_example();
secret_number #(11) U0();
secret_number #(22) U1();
endmodule
PARAMETER OVERRIDE DURING INSTANTIATING

## Slide 18
When instantiating more than the one parameter, parameter values should be passed in the order they are declared in the sub module
1 module ram_controller ();//Some ports
2
3 // Controller Code
4
5 ram_sp_sr_sw #(16,8,256) ram(clk,address,data,cs,we,oe);
6
7 endmodule
PASSING MORE THAN ONE PARAMETER

## Slide 19
In Verilog 2001, the code above will work, but the new feature makes the code more readable and error free
1 module ram_controller ();//Some ports
2
3 ram_sp_sr_sw #(
4 .DATA_WIDTH(16),
5 .ADDR_WIDTH(8),
6 .RAM_DEPTH(256)) ram(clk,address,data,cs,we,oe);
7
8 endmodule
Verilog 2001